## Slide 1
A team can have up to 4 members including the team leader. Add rows if necessary.
Team Details
Team Name:
SR. NO
ROLE
NAME
ACADEMIC YEAR
1
Team Leader
2
Member 1
3
Member 2
4
Member 3
COLLEGE NAME
TEAM LEADER CONTACT NUMBER
TEAM LEADER EMAIL ADDRESS
Team Titans
Noopa Maria Rojan
Final Year
(2026-2027)
Anna Boban
Final Year
(2026-2027)
Haya KT
Final Year
(2026-2027)
Nivya Mathew
Final Year
(2026-2027)
Saintgits College Of Engineering
+91 70257 00386
noopamariarojan@gmail.com

## Slide 2
Problem Statement Addressed
Selected the problem statement your idea addresses
DESCRIPTION / DETAILS
Applied Materials PS02: AI-powered navigation-error recovery for wafer inspection tools — restoring exact microscopic site alignment despite motion-stage drift, thermal expansion, and vibration errors.

## Slide 3
Idea Description
Provide a brief summary of your idea, including the key concept and approach. Provide a brief overview of your solution and how it addresses the problem statement.
KEY CONCEPT & APPROACH
Locates the exact (x,y) coordinates of a 100x reference site inside a 10x search image via scale-aware, sub-pixel NCC matching.
SOLUTION OVERVIEW
Multi-scale correlation with sub-pixel peak fitting and center-tie-breaking recovers navigation accuracy — 100% pass @5px in 38.4ms.

## Slide 4
Proposed Solution
Describe your idea in detail. Include the methodology, technologies involved, and how it addresses the chosen problem statement.
SOLUTION DETAILS
Two-stage pipeline: SEMDataGenerator synthesizes DRAM/FinFET wafer pairs with physical SEM noise (Poisson shot noise, astigmatic blur, charging streaks). DriftSenseLocalizer then applies multi-scale NCC with parabolic sub-pixel refinement and center-proximity tie-breaking for periodic arrays.

## Slide 5
Innovation and Uniqueness
Highlight what makes your idea unique or innovative compared to existing solutions.
KEY INNOVATION
A literature-grounded physics-based SEM data engine paired with a scale-aware sub-pixel localizer whose center-proximity tie-breaking resolves ambiguity in highly periodic DRAM/FinFET arrays.
COMPETITIVE ADVANTAGE
100% pass @5px/@4px (targets 90%/85%), 91.4% at ultra-precision 1px, and 38.4ms mean runtime — inside the 50ms real-time target. Achieved with a lightweight, GPU-free, CPU-only Python pipeline, easy to integrate into existing inspection tools.

## Slide 6
Impact and Benefits
Explain how your solution will make an impact, such as improving performance, reducing costs, increasing efficiency, or solving other challenges.
Primary Impact
Eliminates costly manual re-alignment when inspection tools revisit a microscopic site across dies, recovering navigation accuracy in real time and improving the reliability of downstream yield analysis on the production line.
Quantifiable Outcomes
100% pass @5px & @4px, 97.1% @2px, 91.4% @1px; mean error 0.42px, median 0.28px; 38.4ms mean runtime per pair (target <50ms).

## Slide 7
Technology & Feasibility/Methodology Used
Describe the technologies, methodologies, or tools you plan to use to implement your idea.
IMPLEMENTATION STRATEGY
Pure Python 3.9+ pipeline, config-driven via one JSON file. Modular package (sem_generator.py, localizer.py, optical_extension.py) with CLI entry points for dataset generation and benchmark evaluation. Validated on 35 DRAM/FinFET pairs at 38.4ms mean runtime, no GPU required.
Software Architecture
Hardware Components
Development Tools

## Slide 8
GitHub & Video Link
GitHub Repository
https://github.com/nivyamathew05/Drift-Sense-Wafer-Inspection
Prototype / Simulation Video
https://drive.google.com/file/d/1GPExUj-L78JLCM8_8DE_8dMWTwOlIHKs/view?usp=sharing

## Slide 9
Research and References
Research Background & Methodology
Synthetic data and degradation physics are grounded in published DRAM/FinFET lithography and SEM literature — Poisson shot noise, astigmatic lens blur, and dielectric charging-streak models — for physically realistic benchmarking.
References & Citations
Kim et al. (2020), IEEE Trans. Electron Devices 67(4), 1432-1440.
Auth et al. (2012), IEEE IEDM, pp. 25.1.1-25.1.4.
Reimer (1998); Cazaux (1999), J. Appl. Phys. 85(2), 1137-1147.